## Slide 1
PEER | CSSR | INDIA
PPT 2 -
FIRE FIGHTING
Presented By:- Sachin Chauhan,2IC

## Slide 2: OBJECTIVES
  What is fire and Type.
  Fire fighting technique.
  Types of Combustion, Mode of spread of fire and Stages & Phases of burning.
Upon completing of this lesson, you will be able to :-
1
2
3

## Slide 3: FIRE
A process in which substances combine chemically with oxygen from the air and typically give out bright light, heat and smoke.
Fuel+O2 CO2 + CO

## Slide 4
FIRE AND ITS ELEMENTS: FIRE TRIANGLE
“Three things must be present at the same time to produce fire”
Enough OXYGEN to sustain combustion.
Enough HEAT to reach ignition temperature.
Some FUEL or combustible material.
Together, they produce a CHEMICAL REACTION that results in what we term a “FIRE”.

## Slide 5
FIRE TETRAHEDRON
For combustion to occur, four components are necessary:
    Heat (Source)
    Fuel
    Air (Oxygen)
    Self Sustaining Chemical Chain Reaction
A triangular shape similar to a pyramid but has 3 sides and a base.

## Slide 6
CLASSIFICATION
OF FIRE
Class A :
        Fire involving solid combustible materials of organic nature such wood, paper, rubber, plastic, cloth which requires cooling effect.
Class B :
        Fire involving inflammable liquids or liquefiable solids such as petrol, kerosene, acids, solvent etc.

## Slide 7
CLASSIFICATION
OF FIRE
Class C :
        Fire involving inflammable gases under pressure including liquefied gases such as methane, hydrogen, acetylene, LPG etc.
Class D :
        Fire involving combustible metals, such as magnesium, zinc, sodium, aluminum, potassium, radioactive material etc. When the burning metals are reactive to water.

## Slide 8
FIRE EXTINGUISHING TECHNIQUE:
Extinguishing fire involve the elimination or removal of one or more of the four elements
COOLING:
Removal of heat from the burning material/fire area.

## Slide 9
FIRE EXTINGUISHING TECHNIQUE:
2. SMOOTHERING:
Cutting the supply of oxygen from the fire area.
3. STARVATION:
Removal of un-burnt material or fuel.
4. BREAKING OF CHAIN REACTION:
Interrupt the chain reaction between fuel, heat and oxygen.

## Slide 10
TYPES OF COMBUSTION :
      Slow or incipient combustion- in which the amount of heat & light emitted is feeble.
      Rapid or active combustion- in which a considerable amount of heat & light is emitted within a short time

## Slide 11
TYPES OF COMBUSTION :
  Deflagration – which takes place with a considerable rapidity, evolving heat & light.
  Explosion - a very rapid combustion with a loud noise within an extremely short time with generation of very high pressure & temperature.

## Slide 12
RATE OF COMBUSTION
It is the rate of burning of any substance and measured in length over time like millimeters per sec.
A rate of combustion or the spread of fire would depends on :
The area of solid/liquid in contact with air.
The amount of heat generated to raise the temperature of un-burnt portion.

## Slide 13
RATE OF COMBUSTION
The ability of materials to conduct heat away.
Atmospheric humidity.
Wind velocity.
Temperature.
Atmospheric pressure.

## Slide 14
MODES OF SPREAD OF FIRE
Conduction:
The process by which heat is directly transmitted through the material of a substance when there is a difference of temp bet adjoining regions.
  It occurs only in solids i.e. metallic objects.

## Slide 15
CONDUCTION
Heat energy is passed on from one molecule to the next.
The molecule vibrates above its mean position.
Pass on heat energy by colliding with their neighbors.
The ability to conduct heat varies between materials.
Less Agitated

## Slide 16
CONVECTION
  Transfer of heat by the movement of a fluid (liquid) or gas bet areas of different temp.
  It occurs both in liquids & gases

## Slide 17
RADIATION
  It is neither conduction nor convection. These are heated rays emanating from the hot object.
  It travels at the speed of light.

## Slide 18
RADIATION
It does not involved any contact between bodies
It is independent of any material in the intervening space
These are the heated rays, travels in straight line in all directions with same intensity

## Slide 19
THREE PROGRESSIVES STAGES OF BURNING
Incipient or beginning phase
Free burning phase
Smoldering phase
The products of combustion

## Slide 20
PHASES OF BURNING
It depends on the following factors-
  The amount of time the fire has burnt.
  The ventilation characteristics of the confining structure
  The amount and type of combustibles present.

## Slide 21
INCIPIENT OR BEGINNING PHASE
Oxygen plentiful
Temperature has not built up to high peak
Thermal updraft rises, accumulates at highest point
Breathing not difficult
Fire extinguishments :
  Direct application of water at base of fire.

## Slide 22
FREE BURNING PHASE
Fire has involved more fuel
Oxygen supply is being depleted
Heat accumulated at upper areas
Breathing difficult : Masks recommended
Fire extinguishments is reaching the area of major involvement
Good steam production

## Slide 23
SMOLDERING PHASE
Oxygen supply not equal to demands of fire
Temperature throughout
building is very high
Normal breathing is not possible
Maximum steam production from water fog

## Slide 24
REVIEW
  What is fire and Type
  Fire fighting technique
  Types of Combustion, Mode of spread of fire and Stages & Phases of burning

## Slide 25
ANY QUESTION ?

## Slide 26
EVALUATION
1.How many types of fire are there?
Ans- There are four types of the fire, i.e. A,B,C & D types.
2.How many ways are there for fire to spread?
Ans- There are three ways for spread of fire.
Conduction
Convection
Radiation

## Slide 27
THANK YOU